## Slide 1
1
2
3
4
5
6
7
8
9
10
11
FINAL PITCH
PROBLEM-DATA-GeoAI SOLUTION (PDGS) CANVAS
PROBLEM STATEMENT
STAKEHOLDERS & USERS
SPATIAL CONTEXT
DATA REQUIREMENTS
GeoAI INTELLIGENT
IMPLEMENTATION ROADMAP
VALUE & IMPACT
ETHICS, PRIVACY & SUSTAINABILITY
TECHNOLOGY STACK
GEOAI SOLUTION DESIGN
Project Title: ResiliNet 3D
Team Name: AI Slop Final Boss
Team Code: HACK_MY_060
From Real-World Problems to Intelligent Geospatial Solutions
Virtual Hackathon Submission
On 18 August 2021 a flash flood off Gunung Jerai struck Yan, Kedah: 219 mm of rain in 24 hours, about 4,395 people affected.
When the network fails in that hour, one officer with one portable tower and one generator chooses sites by instinct.
Nothing shows the consequence of a placement before it is committed.
Primary users: the state disaster committee's emergency communications officer, and resilience planners at network operators (MCMC, TM, EDOTCO context).
Beneficiaries: 13 kampungs, about 13,900 estimated residents in the pilot square.
A person decides; the tool ranks and records.
One 8 by 8 km square at Yan, Kedah. A 1,217 m massif carries the district's tower cluster above the coastal plain it serves.
Terrain decides line of sight, one mountain road decides access, floodwater decides both.
Real console render, modelled surge at hour eight.
Analysis grid 15.6 m; six stages, 0 to 1.8 m.
All public and licensed: OpenStreetMap (ODbL) roads, buildings, facilities, kampungs, towers; SRTM terrain via AWS Terrain Tiles; WorldPop 2020 population at 100 m (CC BY); Sentinel-1 radar (Copernicus) for the observed 2021 monsoon water.
No operator data, no personal data; asset costs are labelled demonstration values.
Deterministic geospatial computation, every step inspectable.
HAND hydrology builds the flood surface per stage. A terrain-aware viewshed with 4/3 effective-earth approximates coverage. Road-graph severance tracks access.
A browser engine recomputes the whole future in about 1 ms per placement.
Replay the modelled surge on a 3D block of real terrain and watch who loses service, hour by hour.
Score the four intuitive placements live; all four fail. Rank 137 viable sites by benefit per ringgit.
A four-perspective Scenario Council argues the pick in plain words; the planner accepts, modifies or overrides.
Python precompute: GeoPandas, Rasterio, NetworkX; 31 tests.
Output is a 2.8 MB static pack, no server, no database.
Browser console: TypeScript and three.js; 97 tests.
Runs fully offline from a USB stick, which is the condition of a disaster.
Fairness: the ranked plan leaves Ruat dark, and the screen says so.
Privacy: nothing below 100 m grid cells.
Transparency: six evidence labels on every value; assumptions register A-001 to A-026; published weights.
Accountability: exportable decision log.
Safety: “not a forecast” on screen.
Sustainability: 2.8 MB, offline, modest hardware.
Oversight: a person accepts, modifies or overrides.
Same tower, two sites: 0 people at the district HQ, 1.1 m of water by hour eight; 13,369 at the engine's site.
The cheapest right move is a generator on dark site T-00: 12,228 people back for RM 18,000, RM 1.47 per person.
Checkable before irreversible.
Now: an offline demo of one district, 128 automated tests, a Sentinel-1 pattern check, 63.6% of observed water inside the modelled envelope against 33.9% for chance. Magnitude stays a scenario dial, not a forecast.
Next: river-gauge levels drive the stage dial; operator data under NDA replaces demo values; each new district is one config file.
ResiliNet 3D: see the impact before you spend. The cheaper site wins only while it stays dry and reachable, and this simulator shows exactly when that stops being true.