## Slide 1
1
2
3
4
5
6
7
8
9
10
11
FINAL PITCH
PROBLEM-DATA-GeoAI SOLUTION (PDGS) CANVAS
PROBLEM STATEMENT
STAKEHOLDERS & USERS
SPATIAL CONTEXT
DATA REQUIREMENTS
GeoAI INTELLIGENT
IMPLEMENTATION ROADMAP
VALUE & IMPACT
ETHICS, PRIVACY & SUSTAINABILITY
TECHNOLOGY STACK
GEOAI SOLUTION DESIGN
Project Title: ResiliNet 3D
Team Name: AI Slop Final Boss
Team Code: HACK_MY_060
From Real-World Problems to Intelligent Geospatial Solutions
Virtual Hackathon Submission
Kuala Krai gauge, December 2014: 34.2 m, nine metres above danger. The town an island for five days, two networks down.
The towers did not drown. They lost power, and the fuel road closed first. In our valley 36,614 people lose their phone, 19,595 of them on dry ground.
Nobody can see in time where the one tower and the one convoy should go.
Primary users: the state emergency communications officer; MCMC; the operators whose crews top up sites.
Beneficiaries: the 101,384 people of the Dabong to Kuala Krai valley, counted from WorldPop.
The officer decides; the app ranks and explains.
A 40 by 38 km box, Dabong to Kuala Krai, Kelantan, where the Galas meets the Lebir. One trunk road, one railway, 12 existing sites.
Terrain decides line of sight; the river decides the roads; the roads decide which sites live.
Site stage at 27.0 m: the recommended hill.
62 m grid; same engine for Beaufort and Yên Bái.
All public and licensed: NASA SRTM terrain; Sentinel-2 surface; OpenStreetMap roads, rail, bridges, buildings; WorldPop 2020 people; OpenCellID cells for the 12 sites; the JPS gauge; WeatherNext 3 hourly basin rain with its spread; ERA5-Land and WeatherNext 2 replays.
No operator or personal data; battery hours and river constants are stated assumptions.
AI rain becomes a river level; height above the river turns it into a flood. A road is cut when 150 m goes under. A site dies when its fuel road closes and the battery runs out. Line of sight counts who loses signal.
Report a site down and the chain decides again in 0.2 s.
Three acts. Now: the gauge floods the valley. Forecast: the river curve and the hour the network goes dark. Site: the route wave lights what a truck can reach; hills show the people they bring back.
Two tiers. Local top ups are assumed; the one convoy and the one portable tower are ranked, linked to a surviving site.
Node bake: SRTM, OSM, WorldPop and OpenCellID into a 62 m grid with HAND and viewsheds; Python for Earth Engine and WeatherNext.
Browser: Next.js, three.js. Static site, no server, no keys. Three valleys, one code base.
Runs offline on a laptop in the operations room, which is the condition of a flood.
Transparency: a method sheet lists every source, licence and constant, read from the code.
Honesty: the design storm is labelled synthetic; the 2014 replay shows its misses.
Privacy: 100 m WorldPop cells; no subscriber data.
Oversight: the officer’s report wins over the model.
Sustainability: megabytes, offline, modest hardware.
At 27.0 m, 36,614 people lose their phone by 04:00. Local top ups keep 22,803. Of the 13,811 left, the convoy to Kuala Balah and the tower on Bukit Bedak keep 8,604.
Coordinates in seconds, with a reason the officer can defend.
Report Kuala Balah down and the plan moves to Jelawang: 5,141 kept.
Now: three valleys, three real rain feeds, a December 2014 replay checked against the DID flood maps: IoU 0.52 in Kuala Krai town, 0.55 in Dabong. It under floods the main floodplain, over floods tributaries, and says so.
Next: a live JPS gauge feed, the operator’s site and battery inventory, a rating curve per reach, radio propagation over line of sight.
ResiliNet 3D: the tower does not drown, its power goes. See where the one portable tower and the one convoy keep the most people on a working phone, before the roads close.